## Slide 1: Proposal for Automated Naphtha Blending
09-Jan-2025
TCG Digital Velocity to Value
Contact us: contact@tcgdigital.com
Visit us: www.tcgdigital.com

## Slide 2
Table of Content
04
02
01
Project Background
05
06
Value Proposition
03
Our Understanding of the Scope
Sample Screens and Design
Project Timelines and Commercials
Assumptions and Dependencies

## Slide 3
Project Background
1.

## Slide 4
Currently, the Naphtha blending is carried out by a cross functional team spanning across NCR, NCU, Technology, CBT. This team targets to achieve desired Naphtha quality of about 82-84 volume % Paraffin, Aromatic 3.5 to 4.5 volume % as blended quality. If this quality remains in this range, the throughput and margin are maximized.
The cross functional team prepares the schedule for feedstock blending by calculating from opening, closing stock and the received Naphtha quality & quantity tank-wise to arrive at the desired quality. This is manually maintained in the database and circulated through email. This blending operation is an iterative process which consumes fair amount of time in adjusting the various input parameters making the entire process cumbersome.
Additionally there is not much visibility on the real time quality of Feed Naphtha, Shore-tank Naphtha and blended naphtha.
Project Background

## Slide 5
Our Understanding of the Scope
2.

## Slide 6
Understanding of the Scope (1/3)
Synopsis of the solution :
Use Case 1: Monthly Plan for Naphtha Consumption at NCU
Description: The system will provide a web-based interface to enter, modify, and save the monthly Naphtha consumption plan for the NCU (Naphtha Cracking Unit). This feature supports users in creating an efficient and up-to-date consumption plan.
Use Case 2 : Vessel Arrival Schedule
Description: The system displays the vessel arrival schedule, with an option for users to edit the schedule as necessary.
Use Case 3: Shore Tank information at NCR
Description:
  The Monthly Plan for Naphtha Consumption and the Vessel Arrival Schedule are key factors in determining the loading sequence of Naphtha feedstock tanks.
  If a Naphtha feedstock tank is unavailable for blending, the solution will calculate an expected operational date for availability.
  For active Naphtha feedstock tanks, the system projects the date when the tank will reach the 'dead stock level' and provides recommendations for switching to another tank to maintain continuous blending operations.

## Slide 7
Understanding of the Scope (2/3)
Use Case 4 : Naphtha Cost at Shore Tank and after blending
Description :
  Calculate real time quality , quantity and cost of Naphtha in each tank – to be done daily or on shore tank loading. It will act as a deciding factor in case Naphtha quality to obtain a desired blended Naphtha
  Real-time reporting of calculated price of the Naphtha Blend desired.
  Real-time reporting of calculated price of the blended Naphtha.
Use Case 5 : Naphtha Blending Optimization in NCR
Description:
  Users can specify the desired quantity of paraffin in blended Naphtha, setting a key input parameter for further processing.
  The solution determines the tank input sequence and the Blending to Suction ratio required to achieve the desired blended paraffin level in the shore tanks.
  Continuous monitoring of NIR (Near-Infrared Reflectance) values is conducted, providing recommendations to correct the Blending to Suction ratio if necessary.
  Alerts are raised in case of discrepancies between the NIR reading and the desired blended Naphtha composition.

## Slide 8
Understanding of the Scope (3/3)
Use Case 6 :
Optimal Blend Ratio Alert : Notify the operator when the system recommends an optimal light/heavy naphtha ratio to achieve desired cost and quality.
Quality and Cost Alerts:
  - Daily Quality Report: A daily notification summarizing the quality and cost of naphtha in each tank.
  - Tank Loading Quality Alert: Real-time alert for quality and cost during shore tank loading.
Operational Readiness Alert: Notification if a naphtha feedstock tank is unavailable for blending, with an estimated operational readiness date.
Dead Stock Level Alert:
- Approaching Dead Stock Level: Alert when an active naphtha feedstock tank is approaching its ‘dead stock level,’ allowing for timely refilling or replacement.

## Slide 9
Quality | Quantity
Procurement constraints Procurement plan guided by Budget number (Paraffin, Aromatic). At the same time it is to be noted that desired Naphtha is not readily available in the Market. So, CBT is going for Procurement mix to match budget number and availability in the Market. Generally High Paraffinic Naphtha is sourcing from Import source where as Heavy Naphtha is catered from Domestic source. | Receiving constraints : No Constraints
Operation Constraints 1. Blending Rate: Max rate of blending : 85 TPH, when Tank-E/F is in suction or blending. Max rate of blending : 100 TPH when Tank A/B/C/D is in suction/blending. Minimum Blending Rate to be maintained: Above 40 TPH, for protection of the blending pump. 2. Layering issues for different quality of Naphtha in a single tank: Composition varies in different level of the tank. 3. Naphtha Receiving limitation from HOJ-I/II/III: During receiving from HOJ-I/II/IOCL PLT in Tank E & F, it is not possible to receive from HOJ-III in any tank. While receiving from HOJ-III in Tank B & D, it is not possible to receive from HOJ-I/II/IOCL PLT in any tank. During simultaneous receiving from HOJ-I/II/IOCL PLT & HOJ-III of different quality of naphtha, it is not possible to receive naphtha from HOJ-I/II/IOCL PLT in tank E & F and from HOJ-III in Tank B & D. | Tank availability constraints In the case of maintenance of a tank, a manual input option is to be provided.
Blending rate Constraints Blending Rate: Max rate of blending: 85 TPH, when Tank-E/F is in suction or blending. Max rate of blending: 100 TPH when Tank A/B/C/D is in suction/blending. Minimum Blending Rate to be maintained: Above 40 TPH, for protection of the blending pump. | Blending constraints Heavy Naphtha Lighter Naphtha No Constraints
 | Naphtha Suction constraints No Constraints
Model Constraints
The following buckets – Quality and Quantity were deliberated as the main contributing factors to the overall feed stock blending. The user would require a provision to adjust the boundary parameters of the constraints and manual correction provision for the controllable parameters in case required.

## Slide 10
Sample Screens and Design
3.

## Slide 11
Tank Quality Status
Tank A
Tank B
Tank C
Tank D
Tank E
Tank F
Density
Paraffin
Olefin
Naphthene
Aromatics
IP/NP
Sulphur
Density
Paraffin
Olefin
Naphthene
Aromatics
IP/NP
Sulphur
Domestic Pipeline (IOCL)
Optimized Blending
Blending Simulation
Real-time Tank Quality Status
Saved Recommendations

## Slide 12
Optimized Blending
Domestic Pipeline (IOCL)
Tank A
Tank B
Tank C
Tank D
Tank E
Tank F
Flow Rate
Flow Rate
NCU
Blending Ratio
Quality Parameters
Paraffin
Aromatic
Sulphur
……
Price of blended Naphtha
Loading Sequence of Shore Tank
1
Calculate
Input
Output
4
3
1
2
Recommended Tank 1 for blending
5
1
Recommended Tank 2 for blending
2
Cost of Naphtha in the tank
2
Blending Ratio
3
Price of blended Naphtha
4
Loading Sequence of Shore Tank
5
Tank Quality Status
Blending Simulation
Optimized Blending
1
Desired Quality parameters of blended Naphtha
Save
Saved Recommendations
2
2

## Slide 13
Optimized Blending
Domestic Pipeline (IOCL)
Tank A
Tank B
Tank C
Tank D
Tank E
Tank F
Flow Rate
Flow Rate
NCU
Blending Ratio
Quality Parameters
Paraffin
Aromatic
Sulphur
……
Price of blended Naphtha
Loading Sequence of Shore Tank
Input
Output
2
Input Tank 1 for blending
3
Input Tank 2 for blending
Blending Ratio
Quality parameters for blended Naphtha
Cost of Naphtha in the tank
Loading Sequence of Shore Tank
Optimized Blending
Blending Simulation
1
2
3
1
1
2
3
1
2
Price of the blended Naphtha
3
Blending Simulation
Calculate
Save
4
4
4
Saved Recommendations

## Slide 14
Optimized Blending
Optimized Blending
Blending Simulation
Blending Simulation
Saved Recommendations
Input Tank 1 and Naphtha Cost | Input Tank 2 and Naphtha Cost | Blending Ratio | Quality Parameters of Blended Naphtha | Price of Blended Naphtha | Loading Sequence | Initiated By | Run Date

## Slide 15: Project Timelines and Commercials
4.

## Slide 16
Project Timeline

## Slide 17
Budgetary Commercials
Total cost: Rs. 19.4 Lakhs
Billing will be against the following milestones:
SL # | Milestone | % of Payment
1 | Project Initiation | 20
2 | Submission of system requirement document (SRS) | 30
3 | UAT Initiation | 30
4 | Go-Live | 20
# Please note all fees are exclusive of taxes, surcharge and other Government levies. Arrangement (and expenses) towards all travel, food and lodging of consultants will be made/ borne by HPL.
# Ref: The above fees have been estimated based on the Board approved rate chart for TCG Digital (Refer proposal for Program Budget Approval dated May 2021)
SL # | Role | Approximate MM Envisaged
1 | Business Analyst | 2
2 | QA Analyst | 1
3 | Technical Developer | 4
4 | Project Manager | 1

## Slide 18: Assumptions and Dependencies
5.

## Slide 19: Assumptions and Dependencies
Lighter Naphtha from vessels be stored in 2 out of the 6 tanks. The other tanks would be filled by heavier Naphtha.
There is no stirrer in the tanks, comparatively heavier Naphtha will settle at the bottom and tank will empty from bottom. So mixing is not actually happening. The quality of the mixed Naphtha inside the tank at any time will be the weighted average of the different grades of the Naphtha mixed.
Vessel planning will be made available to TCG Digital team to create the loading sequence plan of the shore tanks.
There is no integration with SAP or any third party system for this solution.
During UAT, all real time data would be made available by HPL for comprehensive testing.

## Slide 20: Value Proposition
6.

## Slide 21: Value Proposition for the solution
The cross-functional team will collaborate on a unified system.
The prediction model will be developed, incorporating constraints that account for CBT(procurement) and downstream NCU requirements.
The system will predict tank stockouts, optimize the naphtha tank loading sequence, and forecast probable naphtha requirement dates.

## Slide 22: Thank You
265 Davidson Ave, Suite 220 Somerset New Jersey 08873 |  |  |  | +1 (732) 515-7376 |  | contact@tcgdigital.com www.tcgdigital.com
TCG Digital Solutions LLC
P
E
W